New Approach and Alternate Criterion for Heat-transfer Analysis of Building

Walls and its Applications

Yu Zhanga, b, * and Xu Zhanga

a Building Design Institute, China Academy of Building Research, Beijing 100013, China.

b Department of Building Science, Tsinghua University, Beijing 100084, China.

* Corresponding author: Tel.: +86 10 6469 4479; E-mail: sdjyzhq@163.com

Abstract: Energy consumed by buildings accounts for approximately one-third of the total energy consumption of the society. Moreover, energy systems employed in buildings emit hazardous pollutants, such as, NOx, PM2.5 and CO2, into the environment. Consequently, increasing the energy efficiency of buildings constitutes an important problem concerning the field of building-energy and environment conservation. Thermal resistance and capacitance are two important thermophysical properties of building walls significantly impacting their heat-transfer performance. Traditional theories concerning these properties, however, face certain limitations—(1) the concept of thermal resistance is only valid for one-dimensional, steady heat conduction without existence of an internal heat source; (2) thermal resistance and capacitance are relevant, and can, therefore, not be used to analyze heat-transfer and storage performance, respectively, of building walls. Based on the entransy-dissipation-based impedance theory, a new approach towards realization of heat-transfer analysis and optimization has been proposed in this study. The weightiness of thermal resistance and capacitance with regard to heat-transfer performance has been described along with deduction of the corresponding substitutional relation via illustrative examples. The proposed approach has been demonstrated to effectively overcome aforementioned limitations of building energy conservation problems.

# Keywords: Heat transfer; thermal resistance; capacitance; entransy; impedance.

1. Introduction

Modern building structures consume too much energy and emit a number of hazardous pollutants, such as NOx, PM2.5, and CO2 into the atmosphere. Consequently, increasing the energy efficiency of buildings constitutes an important problem concerning building energy conservation.

Envelopes of modern buildings result in creation of major heating and cooling loads. Therefore, construction of an appropriate building envelope is an effective means of adjusting the heat-transfer rate and reducing the energy consumption of buildings. Thermal resistance and capacitance greatly impact the heat-transfer performance of building walls, and using these two parameters, one can analyze and optimize the heat-transfer performance of buildings, which in turn, would lead to construction of energy-saving building walls. Extant studies have traditionally used only the thermal resistance and retaining-heat parameters to optimize the construction of building walls. Asan et al. [1, 2] numerically explored the effect of different arrangements of wall materials on the time lag and decrement factor concerning the outdoor-air temperature as well as the relationship between these. Corresponding influencing factors were subsequently determined. Studies by del Coz Dı´az et al. [3, 4], Bouchair [5], and Li et al. [6] investigated optimization of the hollow-brick design based on the concept of equivalent thermal conductivity to realize high heat-insulation performance. However, thermal resistance and the retaining-heat parameter are not entirely independent in unsteady heat-transfer processes. Consequently, these cannot be used to analyze heat transfer and storage performances of building walls.

Recently, Guo et al. [7] proposed the concept of entransy—defined as half the product of internal energy and temperature (G = ½ U × T) (U and T denote the internal energy and temperature of a system). It has been observed that entransy dissipation occurs during heat-transfer processes owing to the existence of thermal resistance. Based on this result, thermal resistance can be defined as the ratio of the entransy-dissipation rate to square of the heat flow, and this definition of thermal resistance can be uniquely determined under a known temperature distribution. The said entransy-dissipation-based thermal resistance has been widely employed in the optimization of heat-transfer processes [8–18].

Based on the entransy method, the proposed study aims at decoupling the   thermal resistance and capacitance with regard to unsteady heat-transfer processes, thereby subsequently illustrating weightiness of these two properties in heat-transfer processes and thence deducing the substitutional relationship between them.

2. Definition of entransy-dissipation-based thermal resistance and capacitance in unsteady heat-transfer processes

For a general heat-conduction process occurring across a wall, the thermal energy conservation equation can be expressed as

(1)

where ρ and cp denote the density and constant-pressure volumetric specific heat of the wall, respectively; T denotes wall temperature; t represents time; and q denotes the heat-flow density. Multiplying both sides of eq. (1) by temperature T yields the balance equation of entransy during heat-transfer processes [19] expressed as

(2)

Terms on the left of the equality in eq. (2) denote the time variation of entransy stored per unit wall volume. Correspondingly, two terms exist on the right of the equality sign. The first denotes entransy transferred from one part of the wall to another while the second refers to the local entransy-dissipation rate during heat conduction. It can be seen from eq. (2) that entransy is dissipated as heat-transfer proceeds from a high-temperature zone of the wall to a low-temperature one.

Introducing the temperature of surrounding air into eq. (2), one gets

(3)

where Te denotes the temperature of surrounding air.

Integrating the entransy balance equation (eq. (3)) over the entire heat-conduction domain and transforming volume integrals to surface integrals over the domain boundary using the Gauss Law, eq. (4) can be obtained.

(4)

where n denotes the unit outward normal vector on the wall surface; Σ denotes surface integral area; Ω represents volume integral area, and S and V denote the area and volume of the wall, respectively.

Based on eq. (4), heat-transfer impedance can be defined in accordance with the thermoelectricity analogy and described as follows by eq. (5).

(5)

(6)

(7)

Here, subscripts 1 and 2 represent the two wall boundaries; Qh represents the total heat flow rate; Φh,R denotes the entransy dissipation rate due to thermal resistance of the wall; and ΔGC represents the entransy variation rate owing to thermal capacitance.

Based on the above discussion, the thermal resistance Rh and capacitance Xh can be decoupled from the heat-transfer process and expressed as follows.

(8)

(9)

The entransy-dissipation-based thermal resistance Rh and capacitance Xh are different from traditional thermal resistance R and retaining-heat parameter S in that the heat-transfer and heat-storage processes can be completely characterized by the thermal resistance Rh and capacitance Xh, respectively.

3. Illustrative example 1: weightiness of thermal resistance and capacitance in with regard to building-wall heat-transfer processes

In accordance with the definition of thermal resistance Rh and capacitance Xh, values of Rh and Xh can be easily calculated for a wall of a given room using eqs. (8) and (9). Subsequently, the weightiness of thermal resistance and capacitance during the heat-transfer process can be determined.

3.1 Calculation model

A simplified two-plate room model [20] was considered in this study. In the said model, the internal wall, floor, and ceiling were modeled as a single plate. An external wall, to where a south-facing window was fixed [21] was modeled using another plate. The transient heat-conduction equation for the said plate modeled could be expressed as follows [21].

(10)

Boundary conditions for eq. (10) can be expressed as [21]

(11)

(12)

The initial condition for eq. (10) can be expressed as [21]

(13)

where ρp, cp,p, and kp denote the density, constant-pressure volumetric specific heat, and thermal conductivity of the plate, respectively; tp refers to the plate temperature; τ and x indicate time and space coordinates, respectively; hout and hin denote convective heat-transfer coefficients corresponding to the outer and inner plate surfaces, respectively, which could be calculated with reference to the ASHRAE Handbook [22]; tout,a and tin,a denote outdoor and indoor air temperatures, respectively, while tp,out and tp,in denote temperatures of the outer and inner plate surfaces, respectively; qr,p,out and qr,p,in represent thermal radiation heat fluxes corresponding to the outer and inner plate surfaces, respectively; Lp denotes plate thickness; and lastly, tp,init denotes the initial plate temperature [21].

Heat-transfer equations for the double-glazed window could be expressed as [21]

(14)

(15)

where ρwin and cp,win denote the density and constant-pressure volumetric specific heat of the window; subscripts 1 and 2 refer to the outer and inner glass layers, respectively; Lwin and twin denote the thickness of glass and it temperature, respectively; qr,win denotes the thermal radiation heat flow density of the window; and lastly, h1,2 denotes the overall heat-transfer coefficient between the two glasses expressed as

(16)

where Uwin denotes the overall heat-transfer coefficient of the window while h*out and h*in refer to convective heat-transfer coefficients of the outer and inner window surfaces, respectively.

The energy-conservation equation is [21]

(17)

where VR denotes the room volume; ρa and cp,a denote the density and constant-pressure volumetric specific heat of air; Qp,j, Qwin, Qd,c, and Qven refer to convective heat-transfer rates between the two plates and indoor air, window and indoor air, heat-transfer rate due to presence of internal heat sources, and that due to natural ventilation. Values of Qp,j, Qwin and Qven could be obtained using following equations.

(18)

(19)

(20)

wherein Ap and Awin denote areas of the plate and window while ACH represents air change per hour.

3.2 Calculation conditions

Table 1 summarizes building parameters. In the following calculations, typical rooms in seven representative Chinese cities located in regions with different climatic conditions were considered (refer Table 2). Climate data for the seven cities were generated using the Chinese Architecture-specific Meteorological Data Sets for Thermal Environment Analysis.

Table 1. Building parameters [20, 21]

| Category | Parameters |
| --- | --- |
| Dimension Wall and window ACH Internal heat sources Convective heat-transfer coefficient | 5.7 m (depth) × 3.6 m (width) × 3.2 m (height) External reinforced concrete: 0.17 m; ρcp = 2.3 MJ/m3 K; k = 2 W/m K External polystyrene board: 0.08 m; ρcp = 0.048 MJ/m3 K; k = 0.047 W/m K External wall plate:0.25 m; ρcp = 1.58 MJ/m3 K; k = 0.14 W/m K Solar radiation absorptance of external wall plate: 0.6 Ceiling and floor: 0.2 m; ρcp = 2.3 MJ/m3 K; k = 2 W/m K Internal wall: 0.2 m; ρcp = 0.84MJ/m3 K; k = 0.41 W/m K Internal wall plate: 0.2 m; ρcp = 1.5 MJ/m3 K; k = 1 W/m K Double-glazing: 2.0 m (length) × 1.7 m (width) Overall heat-transfer coefficient: 3.1 W/m2 K SC = 0.67 (winter), SC = 0.44 (summer) 5.0 h-1 (outdoor temperature measured between 293 K and 299 K) 0.75 h-1 (others) 10.6 W/m2 hout = 23.3 W/m2 K hin = 1.31(△t)1/3 22 |

Table 2. Climatic characteristics of different cities [20] considered in this study

| Regions | Latitude | January |  | July | Climate Type |
| --- | --- | --- | --- | --- | --- |
|  | (o) | Average temperature (◦C) | Average solar radiation (Wm−2) |  | Average temperature (◦C) | Average solar radiation (Wm−2) |  |
| Harbin | 45.75 | -21.8 | 67.4 |  | 22.9 | 209.1 | Severe cold |
| Urumchi | 43.78 | -18.2 | 56.8 |  | 25.0 | 261.6 | Severe cold |
| Beijing | 39.93 | -3.6 | 97.8 |  | 25.3 | 205.0 | Cold |
| Shanghai | 31.17 | 3.7 | 86.7 |  | 29.2 | 188.9 | Hot summer and cold winter |
| Lhasa | 29.67 | -0.2 | 189.8 |  | 15.4 | 270.3 | Cold |
| Kunming | 25.02 | 7.5 | 168.1 |  | 19.5 | 180.0 | Moderate |
| Guangzhou | 23.13 | 9.4 | 103.1 |  | 27.8 | 166.5 | Hot summer and warm winter |

3.3 Results analysis

Calculation results for values of thermal resistance Rh and capacitance Xh of the external wall plate of the building in different cities are depicted in Figs. 1–4. From the figures, it can be concluded that the weightiness of capacitance Xh exceeds that of thermal resistance Rh as regards the building external wall in summer. That is, heat storage plays a significant role in thermal processes that occur in buildings, and that optimization of the heat-storage process is more efficient compared to that of heat-transfer. Meanwhile, it was observed that the value of capacitance Xh was minimum in Harbin, whereas it was maximum in Lhasa.

Using the same method, values of the thermal resistance Rh and capacitance Xh during winter were calculated for the seven different cities. In this case, the weightiness of thermal resistance Rh was observed to exceed that of capacitance Xh for the building external wall, thereby implying that heat transfer plays a major role in the thermal process of buildings during winter, and that optimization of the heat-transfer process during winters is more efficient compared to that of the heat-storage process. As observed, the thermal resistance Rh was minimum in Kunming while that in Harbin was maximum.

Harbin                                    Urumchi

Fig. 1. Thermal resistance Rh and capacitance Xh in Harbin and Urumchi during summer

Beijing                                    Shanghai

Fig. 2. Thermal resistance Rh and capacitance Xh in Beijing and Shanghai during summer

Lhasa                                     Kunming

Fig. 3. Thermal resistance Rh and capacitance Xh in Lhasa and Kunming during summer

Guangzhou

Fig. 4. Thermal resistance Rh and capacitance Xh in Guangzhou during summer

4. Illustrative example (2): Substitutional relationship between thermal resistance and capacitance

Combining eqs. (5)–(9), the following relationship between thermal resistance Rh and capacitance Xh can be deduced.

(21)

It can, therefore, be demonstrated that thermal resistance Rh and capacitance Xh maintains an alternative relationship.

Multiplying both sides of eq. (21) by (T2 - T1) and integrating the equation over the time domain yields

(22)

where Q denotes the total heat transferred from outdoors to indoors in accordance with the building external wall plate.

For given values of k and ρcp of the building external wall plate, the value of Q can be calculated using eq. (22). Likewise, for another value of k, one could calculate the value of ρcp in accordance with eq. (22) under the condition that values k and Q are known.

The same room described in Table 1 was used to illustrate the said alternate relation. Figure 5 depicts the analysis result. As can be observed, the thermal conductivity k and constant-pressure volumetric specific heat ρcp of the building external wall plate in Beijing over an entire year demonstrates an approximate quadratic-function distribution.

Fig. 5. Substitutional relationship between k and ρcp in Beijing over a one-year duration.

5. Conclusions

Entransy-dissipation-based thermal resistance and capacitance of a building wall during unsteady heat transfer have been defined and decoupled in the proposed research. Accordingly, solutions to the following problems can be obtained.

(1) The weightiness of thermal resistance and capacitance during unsteady heat-transfer processes can be determined to guide the optimization of building wall structures. The heat-transfer and heat-storage processes can, accordingly, be pertinently optimized for transient heat-transfer problems.

(2) An alternate relationship between thermal resistance and capacitance can be established, and the same can be used to construct economical wall structures under the premise of ensuring optimum thermal performance of buildings.

(3) The proposed study provides a novel and in-depth view towards understanding unsteady heat-transfer processes, thereby addressing several problems related to building energy conservation.

Acknowledgements

The author(s) disclosed receipt of the following financial support for the research, authorship, and/or publication of this article: the Youth Science Research Foundation of China Academy of Building Research (20160118331030053).

Reference

[1] Asan H. Investigation of wall’s optimum insulation position from maximum time lag and minimum decrement factor point of view. Energy and Buildings 2000; 32: 197-203.

[2] Asan H. Numerical computation of time lags and decrement factors for different building materials. Energy and Buildings 2006; 41: 615-620.

[3] del Coz Dı´az JJ, Garcı´a Nieto PJ, Betego´n Biempica C, Prendes Gero MB. Analysis and optimization of the heat-insulating light concrete hollow brick walls design by the finite element method. Applied Thermal Engineering 2007; 27: 1445-1456.

[4] del Coz Dı′az JJ, Garcı′a Nieto PJ, Sua′rez Sierra JL, Pen˜uelas Sa′nchez I. Non-linear thermal optimization and design improvement of a new internal light concrete multi-holed brick walls by FEM. Applied Thermal Engineering 2008; 28: 1090-1100.

[5] Bouchair A. Steady state theoretical model of fired clay hollow bricks for enhanced external wall thermal insulation. Building and Environment 2008; 43: 1603-1618.

[6] Li LP, Wu ZG, Li ZY, He YL, Tao WQ. Numerical thermal optimization of the configuration of multi-holed clay bricks used for constructing building walls by the finite volume method. International Journal of Heat and Mass Transfer 2008; 51: 3669-3682.

[7] Guo ZY, Zhu HY, Liang XG. Entransy-a physical quantity describing heat transfer ability. International Journal of Heat and Mass Transfer 2007; 50: 2545-2556.

[8] Chen Q, Zhu HY, Pan N, Guo ZY. An alternative criterion in heat transfer optimization. Proceedings of the Royal Society A-Mathematical Physical ＆Engineering Sciences 2011; 467: 1012-1028.

[9] Chen Q, Wang MR, Pan N, Guo ZY. Optimization principles for convective heat transfer. Energy 2009; 34: 1199-1206.

[10] Chen L, Chen Q, Li Z, Guo ZY. Optimization for a heat exchanger couple based on the minimum thermal resistance principle. International Journal of Heat and Mass Transfer 2009; 52: 4778-4784.

[11] Guo ZY, Liu XB, Tao WQ, Shah RK. Effectiveness–thermal resistance method for heat exchanger design and analysis. International Journal of Heat and Mass Transfer 2010; 53: 2877-2884.

[12] Shah RK, Skiepko T. Entropy generation extrema and their relationship with heat exchanger effectiveness–number of transfer unit behavior for complex flow arrangements. Journal of Heat Transfer; Transactions of the ASME 2004; 126: 994-1002.

[13] Wu J, Cheng XT. Generalized thermal resistance and its application to thermal radiation based on entransy theory. International Journal of Heat and Mass Transfer 2013; 58: 374-381.

[14] Chen Q, Yang KD, Wang MR, Pan N, Guo ZY. A new approach to analysis and optimization of evaporative cooling system I: Theory. Energy 2010; 35: 2448-2454.

[15] Chen Q, Pan N, Guo ZY. A new approach to analysis and optimization of evaporative cooling system II: Applications. Energy 2011; 36: 2890-2898.

[16] Zhang T, Liu XH, Zhang L, Jiang Y. Match properties of heat transfer and coupled heat and mass transfer processes in air-conditioning system. Energy Conversion and Management 2012; 59: 103-113.

[17] Chen L, Chen Q, Li Z, Guo ZY. Moisture transfer resistance method for liquid desiccant dehumidification analysis and optimization, Chinese Science Bulletin 2010; 55: 1445-1453.

[18] Xu YC, Chen Q. An entransy dissipation-based method for global optimization of district heating networks. Energy and Buildings 2012; 48: 50-60.

[19] Zhang Y, Chen Q, Zhang YP, Wang X. Exploring buildings’ secrets: The ideal thermophysical properties of a building’s wall for energy conservation. International Journal of Heat and Mass Transfer 2013; 65: 265-273.

[20] Zeng RL, Wang X, Di HF, Jiang F, Zhang YP. New concepts and approach for developing energy efficient buildings: ideal specific heat for building internal thermal mass. Energy and Buildings 2011; 43: 1081-1090.

[21] Zhang Y, Zhang YP, Wang X, Chen Q. Ideal thermal conductivity of a passive building wall: Determination method and understanding. Applied Energy 2013; 112: 967-974.

[22] ASHRAE. Handbook Fundamentals. SI Edition, Atlanta: American Society of Heating, Refrigerating and Air-Conditioning Engineers, 2009.